## Slide 1: Deformable models for medical image segmentation
Mr. Sc. Marko Subašić

## Slide 2: Contents
Deformable models
Abdominal aortic aneurysm (segmentation, problems)
Segmentation time reduction
4 approaches for AAA segmentation
Conclusion

## Slide 3: Deformable models
Deformable models are curves or surfaces defined within an image domain that can move under the influence of internal forces, which are defined within the curve or surface itself, and external forces, which are computed from the image data.

## Slide 4: Deformable models
The internal forces are designed to keep the model smooth during deformation
The external forces are defined to move the model toward an object boundary or other desired features within an image.

## Slide 5: Deformable models
DMs often combine several image processing methods and incorporates prior information about object being segmented
Robustness to both image noise and small boundary gaps
The goal is to describe the object in the image using a mathematical model

## Slide 6: Deformable models
Initial deformable model is deformed toward its final shape with the help of various factors
Very successful application in medical image segmentation
Possible application in 2-D space and also in higher dimensional spaces

## Slide 7: Deformable models
PARAMETRIC
First type of deformable model
Model is given in parametric form
Problems:
  Unable to segment complex objects in a straight forward manner
  Unable to change topology
GEOMETRIC
More recent date
Evolution of DM depends on geometric properties rather then parameterization
Solves problems of parametric DMs
  Changes topology
  Can model complex shapes

## Slide 8: Geometric deformable models
Based on curve evolution theory or minimization of energy
Utilizes level set algorithm
The curve is represented implicitly as a set of zero valued points
Drawback is higher complexity due to increased number of computations

## Slide 9: Geometric deformable models
The difference between various models

## Slide 10: Example

## Slide 11: Abdominal aortic aneurysm
Enlargement of abdominal aorta due to weakened aortic wall
Enlargement of aorta may lead to aortic wall rapture
Useful information can be obtained through imaging
bifurcation
iliac arteries
renal arteries
aneurzsm
aorta

## Slide 12: Abdominal aortic aneurysm
Current imaging gold standard is Computerized tomography – angiography
It is necessary to extract abdominal aorta from the rest of the abdomen in CT slices – segmentation.
Segmentation results can provide useful information about aneurysm shape, size etc.
  This information is useful in diagnostics, procedure planning, and condition tracking

## Slide 13: Problem
Segmentation of aortic interior and aortic wall is required
  Segmentation of aortic interior is not a difficult task
  Segmentation of aortic wall is much more problematic

## Slide 14: Segmentation of outer aortic border
Calcium sediments – calcifications – can appear inside aortic wall
  High intensity in CT scans, but still part of the aortic wall
In some places aorta may touch surrounding tissue making the border between them difficult to distinguish
  This also poses problem to radiologists

## Slide 15: Decrease of segmentation time
It is desired to decrease number of necessary calculations, especially in 3-D cases
Limit calculations only to DM segments that area actually moving.
  If DM has stopped at a certain point no further calculations need to be done for that point
    Introduction of tracking algorithm for DM
    Points where DM has stopped are excluded from further calculations
  Large decrease of execution time in segmentation of tube like objects like aorta

## Slide 16: Decrease of segmentation time
Multi resolution approach
  Scaling of x and y dimensions
  z dimension is not scaled
Scaling by factor 2 in x and y dimension decreases number of points and number of calculations by 4
After segmentation has been finished at lower resolution it is continued at full resolution for several iterations
  After switching to full resolution function  is decreased by 1 to avoid spilling of DM

## Slide 17: 1st approach
Segmentation of aortic interior is performed with 3-D DM and poses no significant problem
  These segmentation results can be used as initialization for aortic wall segmentation
In segmentation of aortic wall knowledge of aortic wall and segmented aortic interior are used
  The shape of the aneurysm is difficult to predict but we can presume that the outer aortic border is smooth
  Centers of mass of aortic interior and aortic wall should be nearby
  2-D deformable model used in segmentation

## Slide 18: 1st approach
Additional stopping criterion

## Slide 19: 1st approach
Speed function

## Slide 20: 1st approach
Results

## Slide 21: 2nd approach
Segmentation of aortic interior same as in the 1st approach – 3D DM
In segmentation of aortic wall tracking of moving segments of DM is introduced
  2-D deformable model is used
  tracking of stretching

## Slide 22: 2nd approach
Additional stopping criterion
  Moving curve segment is bounded with stationary points – tracking of moving segments (merging and splitting)
  Extension coefficient
  Spread coefficient:
  Stopping condition:
1
3

## Slide 23: 2nd approach
Results

## Slide 24: 3rd approach
Segmentation of aortic interior and aortic wall using 3D DM
Stopping of DM penetration into surrounding tissue in aortic wall segmentation – preprocessing
  Slice by slice reconstruction of outer aortic border with some information flow among neighboring slices

## Slide 25: 3rd approach
Reconstruction of aortic wall
  Conventional methods are use to enhance outer aortic border
  In reconstruction of weak outer border knowledge of aortic shape and aneurysm is utilized

## Slide 26: 3rd approach
Quasi-convexity
  Distance map and its gradient in radial direction is used

## Slide 27: 3rd approach
Calcifications – sediments of calcium inside aortic wall
  Very bright regions on CT slices – introduces inhomogeneity into aortic wall region
  Can be used in estimation of position of weak outer aortic border

## Slide 28: 3rd approach

## Slide 29: 3rd approach
Results

## Slide 30: 3rd approach
Results

## Slide 31: 4th approach
Segmentation of aortic interior and aortic wall using 2-D DM
  Aortic interior: edge based DM
  Outer aortic boundary – aortic wall: region based DM
Slice by slice segmentation with information flow among neighboring sliced
Additional modifications to overcome problems in aortic wall segmentation

## Slide 32: 4th approach
Initialization of DM in aortic interior segmentation using neighboring, already segmented slices
Non-serial slice sequence in segmentation
Initialization in aortic wall segmentation using segmentation results of aortic interior

## Slide 33: 4th approach
Speed function in region based DM holds 5 terms:
Constant speed term – constant expansion of DM
Curvature based term – elastic properties

## Slide 34: 4th approach
Term that enforces curvature similarity of inner and outer aortic border
Image based component – only similar pixels are allowed
Term based on neighboring, already segmented slices

## Slide 35: 4th approach
Results

## Slide 36: 4th approach
Comparison with manually corrected semiautomatic method
  Mean correlation coefficient 0,86
  Mean relative error 35,39%
  Standard deviation of relative error 19,68%

## Slide 37: Conclusion
Four methods have been presented for segmentation of abdominal aortic aneurysm that require minimal user intervention.
All four methods are based on geometric deformable model
Methods differ in a way of solving the specific problem of aortic wall segmentation
Methods have been tested on patient data

## Slide 38: Conclusion
Possible application of the methods is in diagnostics, procedure planning and condition tracking
All four methods do not function well in the presence of strong image degradation such as artifacts produced by metal parts of stent graft device
  It is not possible to use these methods in postoperative condition tracking
Most successful is the method that utilizes knowledge of aortic shape