## Slide 1
Neural Speaker Embeddings for Ultrasound-based Silent Speech Interfaces

## Slide 2
Goal: to reconstruct the speech signal from a recording of the articulatory movement
Data acquisition techniques:
  Ultrasound Tongue Imaging (UTI)
  Electromagnetic Articulography (EMA)
  Permanent Magnetic Articulography (PMA)
  surface Electromyography (sEMG)
  Magnetic Resonance Imaging (MRI)
  lip video, …
Application: Silent Speech Interface (SSI)
  For speaking impaired people
  For extremely noisy conditions
  …
1. Articulatory-to-acoustic conversion
Ultrasound Tongue Imaging (UTI)
  Records a sequence of images (64x842) at a frame rate of 82 fps
  Problem: the images are very speaker-specific
The TaL80 database (Renals et al.)
  Parallel ultrasound, speech and lip video recordings from 80(+1) speakers
  Goal of the paper: speaker recognition and normalization experiments

## Slide 3
Performs the conversion in 2 steps
1st step: A DNN estimates a mel-spectrogram from the sequence of UTI video frames
  We have synchronized input (UTI) and target (speech) signals
  Our DNN operates in a synchronized (frame-by-frame) manner
  But sequence-to-sequence mapping would also be possible
2nd step: Converting the mel- spectrogram to a speech signal
  Important task in neural speech synthesis
  Large pre-trained DNN models exist for this, we used WaveGlow
2. Our Current UTI-to-Speech SSI model
Structure of the DNN
  Input: a block of 21 consecutive UTI frames
  Output: one frame of the mel-spectrogram
  The network has a special 3D-CNN structure
    Conv3D over 5-frame local blocks, fusing the information along time only at a higher stage
    Motivated by the TDNN popular in ASR, and by the ”(2+1)D” CNN model of Tran et al.

## Slide 4
Goal: to extract a vector from each utterance that represents the speaker’s characteristics
  Useful for speaker recognition, or to normalize the sentences wrt. speakers for other tasks
X-vector: a popular solution (for speech signals)
  A DNN is trained to classify speakers
  But it should also work for for unseen speakers
    So an upper hidden layer is used to provide the x-vector (instead of the softmax output layer)
  It should give a fixed-size vector independent of the input duration
    The network consists of a frame-level part, a pooling step, and an utterance-level part
  Typically trained on huge databases with thousands of speakers
3. Speaker Embedding Vectors
We adapted the x-vector approach to UTI videos
  Frame-level part: the same structure as the 3D-CNN used for SSI
  Statistical pooling: averaging along time
  Sentence-level: 2 fully con- nected layers (FC#1, FC#2)
  Output layer: Softmax (size= no. of speakers)
The x-vector is obtained as the (linear or non-linear) output of FC#1 or FC#2
The network was trained to classify speakers
  Training data: samples from 50 speakers of the TaL80 corpus

## Slide 5
Speaker classification accuracy of the network
  For the same 50 speakers used for training
  But on an independent development set
  Using the softmax output layer
Error rates as a funtion of the input chunk length
We obtained very low error rates
  Already for short input durations
  Further improvements when increasing the length
Justifies that the videos are very speaker-specific
4. Speaker Recognition Results
Does the results generalize to unseen speakers?
  Evaluating the model on the 31 held-out speakers
  The softmax output layer can no longer be used
Recognizing new speakers based on the x-vector
  Would require the building of a complex speaker recognition system, but we wanted to avoid this
Simplest evalutation method: distance comparison of same-speaker and different speaker x-vector pairs
  We used the cosine distance, as it is frequently used in speaker classfication
Another simple method: applying a classifier
  with the x-vector as input
We intentionally used a simple classifier (1-NN)
  sensitive to the underlying data and distance function

## Slide 6
Cosine distances for randomly selected same-speaker and different-speaker x-vector pairs
  For samples from the 31 held-out speakers
There is some overlap
But the distance is typically much larger between different speakers than for same-speaker samples
So the x-vectors behave as expected
5. Speaker Recognition Results #2
Speaker classification results using 1-NN
  Using the cosine distance
  Over the samples of the 31 held-out speakers
We performed leave-one-out experiments:
  For each vector, find the closest one (exluding itself)
  The result was considered correct if the two segments had the same speaker ID
The obtained error rates:
  Extracting the x-vector from either FC#1 and FC#2
  Using either the linear or the non-linear output
  The error rates are low, the x-vector seems to work well for speakers not seen during training

## Slide 7
Our SSI system creates intelligible speech with good quality – in a speaker-dependent manner
  But quality drops drastically for multi-speaker data
Can we use the x-vectors to improve our SSI ?
  Supporting the normalization of the images
  By using the x-vector as auxiliary input (similarly to how x-vectors used in ASR)
The optimal combination of the SSI input and the x-vector is not trivial
  The UTI images should be processed by convolution
  But the x-vector is not an image…
  We processed the UTI and the x-vector by separate layers, combining them only at a higher level (after the convolutional layers)
  But this is quite probably suboptimal
6. Speaker Normalization Attempts
Results: MSE of the SSI network
  Using one-speaker or multi-speaker data sets of about the same size
  The x-vector DNN is trained on the 50 speaker set
  The SSI DNN is trained and tested on 31 speakers
  The error of the multi-speaker model is more than double than that of the single-speaker model
  The improvement due to the x-vector is negligible 
Conclusion
  The x-vector approach itself seems to be fine
  But the incorporation into the SSI needs improvement

## Slide 8
Thank you for your attention!